## Slide 1
Ergonomic standards
Formation

## Slide 2: Introduction
Ergonomics are a strong pillar to
implement the 5S methodology
Improve work conditions and results

## Slide 3: Cycle time calculation – OCOTDAC Method
OCOTDAC (Observe, Choose, Observe, Think, Decide, Act, Control)
Observe : Basic observations
Choose: Selection of the workbench
Observe: Detailed observations
Think: construction / modification of project
Decide: First estimated assessment
Act: Practical realization of the new workbench
Control: Result control and issues solving

## Slide 4: Cycle time calculation - Work time determination
4 possible methods regrouped in 2 families:
Direct observation methods
  Timing analyzing
  Sample measurement
Predetermination of the times
  MTM (Method Time Measurement)
  Standard data

## Slide 5: Cycle time calculation - Timing analysis
Different steps:
Select operations and the operator to observe.
Divide the work in sub elements.
  Repetitive task
  Occasional task
  Manual task
  Machine task
  …
1
2

## Slide 6: Cycle time calculation - Timing analysis
Define the necessary number of measures
  10 minimal observations for less than 2 minutes cycle times
  5 observations for more than 2 minutes cycle times
Statistic manner :
The total number of measurements depends on 3 factors :
    confidence interval
    Data variability
    Wanted precision degree.
3

## Slide 7: Cycle time calculation - Timing analysis
Measure taking
2 golden rules for direct measure
  Staff must be aware and agreed with the project.
  The timing must be done in normal manufacture conditions.
3 measurement techniques
  Continuous taking
  Sequenced taking
  3 watches system taking
Measure taking difficulties:
  Missing elements
  Analyst sees elements which are not part of the standard cycle.
  A stranger element appears during the cycle.
4

## Slide 8: Cycle time calculation - Timing analysis
Observed time calculation To
3 techniques :
  Mean technique
  Frequency technique
  Michelin technique  Often used in great series.
Stability rate measure:
Application of the values’ appearance and efficiency
  Appearance judgment (AJ)
Under 50%, we can consider that the post is stable.
5
6
  AJ= Speed observed / reference speed

## Slide 9: Cycle time calculation - Timing analysis
Theorical time calculation (Th)
7

## Slide 10: Cycle time calculation - Recapitulative tables
Timing analysis | 
Advantages | Disadvantages
Permits the analyst to see the whole cycle and identify progress sources. The only method to measure the real actual time to realize a task. Fast to identify a first-time base. Relatively simple to implement and explain. Provides values quickly for machine operations | Requires a performance rate depending on operator skills and effort. Requires many observations on different operators. Not so useful on non-repetitive operations Requires a person per operator to perform the analysis

## Slide 11: Cycle time calculation - Recapitulative tables
Sample measurement | 
Advantages | Disadvantages
No timing No need of a permanent presence near the operator Exclude the issue of constant observation on a long time. Represents the mean time whatever the conditions Ideally appropriated for machine operations studies Can be used with a performance rate | Based on the hypothesis that the operator uses an acceptable and standard work method without behavior modification Requires an analysis on many work categories Not profitable if used on an unique post

## Slide 12: Cycle time calculation - Time predetermination
We can predeterminate times thanks to movement analysis (practicable for manual operations)
5 steps:
1.Separation of each task’s movements
2.Determination of each movements’ variables
3.Codification of each movement
4.Reconstitution of movement’s needed times thanks to tables
5.Détermination of operation’s times

## Slide 13: Cycle time calculation - Recapitulative tables
Time predetermination | 
Advantages | Disadvantages
Force to be precise in analysis. Permits to compare several methods to perform a new task. Stimulate movement simplification. Exclude performance rate need. Permits to establish times before the production. Safe and reliable method Permits to easily update time data depending on methods’ changes. Permits to measure the time of little movements. Define a standard language for every operation | Depends on the task description’s precision. Requires formation time. Harder to explain to workers. Requires chrono-analysis or time standards for “machine” times

## Slide 14: Cycle time calculation - Recapitulative tables
Standard data | 
Advantages | Disadvantages
Supplies a mean performance rate Permits to establish times before the production Safe and reliable method Permits to quickly and cheaply establish standards Permits to easily update time data depending on methods’ changes. | Requires important funding to establish the first version Not reliable for little variations in method changings Requires good competences from the analyst to understand complex formulas Hard to explain to workers

## Slide 15: Cycle time calculation - Other times
Other times exist:
Technologic time
Frequential time
Human time
Hidden time
Preparation time

## Slide 16: Workbenches ergonomics – Rules for movement
22 rules exist for movement ergonomics :
Movement simultaneity
Minimal energy spent
Living force
Rythm
Order in the equiped work area
Use of the seriousness
Workbench comfort and lighting
Hand’sliberty
Combine/ Put in place
Finger Load
Control Units

## Slide 17: Workbenches ergonomics – Ergonomics standards
The ergonomics standard, co-construction for the improvement of working conditions and the prevention of arduous work.

## Slide 18: Workbenches ergonomics
Working posture :
 Posture is the first thing to define.
The most frequent strain factor is the working posture set according to the workstation design.

## Slide 19: Workbenches ergonomics – Seat
The choice of the seat will depend on:
  task constraints
  posture flexibility
  ease to sit and stand
  seat stability required
  material covering
  ease to be adjusted
Seated and high-seated positions

## Slide 20: Workbenches ergonomics – Seat
Specific Recommendations exist:
  Easily adaptable
  Provide support and comfort
  prevent sweat accumulation and electrostatic discharge
  Back rest adjustable in height and inclination
  Base should have 5 bearing points to ensure stability.
  Adjustment devices, enabling seat to be adapted to work situation, should be easy to manipulate and reliable. Correct seat adjustment requires operator to be informed and made aware of risks.

## Slide 21
8 Fundamental Ergonomic Principles for better work performance:
Principle 1. Maintain Neutral Posture
Principle 2. Work in the Power / Comfort Zone
Principle 3. Allow for Movement and Stretching
Principle 4. Reduce Excessive Force
Principle 5. Reduce Excessive Motions
Principle 6. Minimize Contact Stress
Principle 7. Reduce Excessive Vibration
Principle 8. Provide Adequate Lighting

## Slide 22: Workbenches ergonomics – Workstation dimensionning
Clearance for passing legs and
feet beneath

## Slide 23: Workbenches ergonomics – Working height and Worktop

## Slide 24: Workbenches ergonomics – Workstation material replenishment

## Slide 25: Workbenches ergonomics – Working zones
Seated Standed
Arduous zone
Acceptable zone
Comfort zone
Comfort zone
Acceptable zone

## Slide 26: Workbenches ergonomics – Zones of vision

## Slide 27: Workbenches ergonomics – Visual range
D (mm) | Between  And  | 0 500 | 500 800 | 800 1250 | 1250 2000 | 2000 3150 | 3150 5000 | 5000 8000
H (mm) |  | 3 | 3.5 | 4.5 | 6 | 9 | 14 | 23
W (mm) | Between  And  | 2 3 | 2 3.5 | 2.5 4.5 | 3.5 6 | 5 9 | 8 14 | 12 23
t (mm) | Dark on light Light on dark | 0.3 0.25 | 0.35 0.3 | 0.45 0.4 | 0.6 0.5 | 0.9 0.75 | 1.4 1.2 | 2.3 2
D = eye distance to the character H = height of the character W = width of the character t = line thickness

## Slide 28: Workbenches ergonomics – Positionning of controls
Recommendations:
Used at each cycle  located in acceptable gripping zones.
The degree of force to be applied should be considered
Used frequently  located near the visual task.
used for emergency operation  very short time actuation
Requires only a single hand  on the side of the limb required (possibility of adaptation for right/left-handed)
Low probability to be actuated accidentally
Controls should locate according to:
  expected operator response time
  potential of emergency reaction (activate E-stop)
  operator learning curve
  handling constraints
Arrangement of controls can minimize postural constraints but, in some cases, can increase the risk of identification errors. Controls must be protected if they could be accidentally activated

## Slide 29: Workbenches ergonomics – Screen and keyboard
Must not be subjected to direct light
Terminal remote from machine
Top and bottom tiltable screen.
Eye-screen distance suited to character vertical dimension.
If Plexiglas protection is required, it should be concave to prevent reflection

## Slide 30: Workbenches ergonomics – Office work

## Slide 31: Workbenches ergonomics – Cycle time

## Slide 32: Workbenches ergonomics – Body movement
Try to limit extreme postures & repetitive movements
Consider exerted forces
Avoir using the hand as :
  A hammer
  Pliers
  Press

## Slide 33: Workbenches ergonomics – Manutention gesture recommendations

## Slide 34: Workbenches ergonomics – Illumination
Lighting homogeneity
Dazzle elimination
Contrasts
Too much light can generate uncomfortable glares and unbalanced illumination.
One light generates a large overhead shade
Two lights soften the shadow
A large lighting equipment minimize the shadow

## Slide 35: Workbenches ergonomics – Noise
Noise level should allow for verbal communication requirement and task complexity.

## Slide 36: Workbenches ergonomics – Thermal environment
Ventilation
  Air renewal rate : 2volumes/h minimum
Air-conditinning
  Air renewal
  Maintained temperature
  Maintained atmospheric composition
 | Winter conditions | Summer conditions
Operating T° | >19°C | <25°C
Air relative humidity | 30-70% | 30-70%
Air velocity | <0.15m/s | <0.25m/s
Vertical gradient | <3°C (feet-head) | <3°C (feet-head)

## Slide 37: Workbenches ergonomics – Anthropometric models
Facilitate an elementary approach to problems of congestion, reach, posture and comfort, when designing equipment.
Model based on the physical body size of most of the population.
Suggested dimensions are derived from known measurements for the fit adult population.
More specific and accurate measurements should be used for in-depth ergonomic design.
Working zones should be adjusted for 90% of the population.
The frequency of the distribution for the stature will depend on the population and it can vary from one country to another.
The anthropometric values considered for a particular country or region may not be suitable for other countries or regions depending on the local physical characteristics

## Slide 38: Workbenches ergonomics – Anthropometric models
Short man / Average woman

## Slide 39: Workbenches ergonomics – Anthropometric models
Tall man

## Slide 40: Workbenches ergonomics – Anthropometric models
Average man / Tall woman

## Slide 41: Workbenches ergonomics – Anthropometric models
Short woman

## Slide 42
VIDEO CHANGEMENT DU WORKBENCH

## Slide 43
Thank you for your attention
Questions ?